## Slide 1
Deliverable 1
Data Analysis — Parkinson's Disease Gait Signal Detection
Project: State Space Models (Mamba) for Medical Time Series
Dataset: PhysioNet — Gait in Parkinson's Disease | N=166 | 5-Fold CV
May 2026 | FAU Erlangen-Nürnberg | Technische Fakultät

## Slide 2: Agenda
02
05
03
04
06
07
08
11
09
10
12
Subheadline möglich. Gegebenenfalls löschen.
01
01
Dataset Overview
Demographics from Excel + fold distribution
02
Signal Visualization
Raw VGRF traces & variability comparison
03
Feature Extraction
TSFresh + manual features, z-score normalisation
04
Dimensionality Reduction
PCA and t-SNE (left / right / combined)
05
Alternative Approaches
UMAP, statistical tests, feature heatmap
06
Discussion & Findings
Key observations and next steps
Agenda — Deliverable 1: Data Analysis

## Slide 3
01
Dataset Overview
Demographics · Cohort Structure · Label Distribution

## Slide 4
Dataset Demographics — Full Dataset (N=166)
Source: demographics.xls
01 · Dataset Overview
Full Dataset (from demographics.xls)
PD (n=93)
HC (n=73)
Male / Female
58 / 35
40 / 33
Age mean±SD
66.9 ± 9.7 yrs
63.3 ± 8.0 yrs
Height mean±SD
1.68 ± 0.10 m
1.68 ± 0.08 m
Weight mean±SD
72.3 ± 11.8 kg
72.3 ± 11.4 kg
H&Y mean±SD
2.26 ± 0.34
—
UPDRS-M mean±SD
18.0 ± 9.6
—
Per-Cohort Breakdown
Cohort
PD
HC
Total
Condition
Age PD
Ga (Yogev)
29
18
47
Normal walk
61.6±8.8
Si (Frenkel-Toledo)
35
29
64
Treadmill
67.2±9.1
Ju (Hausdorff)
29
26
55
RAS walk
66.8±10.8
[INSERT IMAGE] fig_A_demographics_full.png (Age histogram + cohort bar chart + H&Y distribution)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
4/18

## Slide 5
Dataset Demographics — 5-Fold Split (Fold 1 shown)
Source: splits/Fold_1/
01 · Dataset Overview
Fold 1 Summary (training + test combined)
PD
HC
Total
Total Subjects
40
40
80
Ga Cohort
14
11
25
Si Cohort
10
17
27
Ju Cohort
16
12
28
H&Y 2.0
19
—
19
H&Y 2.5
14
—
14
H&Y 3.0
7
—
7
⚠ Cohort Confound Note
• 3 sub-cohorts (Ga/Si/Ju) collected under different conditions:
— Ga: normal walking on level ground
— Si: treadmill walking
— Ju: walking with rhythmic auditory stimulation (RAS)
• Cohort condition may explain more PCA variance than diagnosis
• → PCA/t-SNE panels B always show cohort colouring to detect this
• Imbalanced severity: H&Y 2=19, H&Y 2.5=14, H&Y 3.0=7 subjects
• → SMOTE applied on training folds only to address imbalance
[INSERT IMAGE] fig_B_demographics_fold.png (Age histogram + cohort bar + mean±SD chart)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
5/18

## Slide 6
02
Signal Visualization
Raw VGRF Traces · Force Variability · PD vs HC Comparison

## Slide 7
Raw VGRF Signals — PD vs Healthy Controls
15 seconds of total force, left and right foot
02 · Signal Visualization
Vertical Ground Reaction Force (VGRF) captures the force each foot exerts on the ground. 16 sensors per foot at 100 Hz. Coefficient of Variation (CV) shown per trace.
[INSERT IMAGE] fig_C_raw_signals.png (3 PD + 3 HC subjects × 2 feet. CV annotated per trace. Higher CV = more irregular gait rhythm in PD.)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
7/18

## Slide 8
Gait Force Variability — PD vs Healthy Control
Rolling mean ± SD (5s window, 2.5s step)
02 · Signal Visualization
Key finding (Yogev et al., 2005): In healthy adults, gait rhythmicity is automatic — stride variability is unaffected by cognitive load. In PD, variability increases markedly under dual-task conditions, indicating a loss of automaticity.
[INSERT IMAGE] fig_D_variability.png (1 PD + 1 HC × 2 feet. Raw signal + rolling mean (navy) + mean±SD band (blue). CV shows higher irregularity in PD.)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
8/18

## Slide 9
03
Feature Extraction
TSFresh · Manual Features · Z-Score Normalisation · Per-Subject Statistics

## Slide 10
Feature Extraction Pipeline
Windowed extraction → per-subject statistics → z-score normalisation
03 · Feature Extraction
TSFresh (Primary Approach)
• Library: tsfresh (EfficientFCParameters)
• ~750+ features per channel per window
• Window: 5 seconds (500 samples)
• Step: 2.5 seconds (50% overlap)
• Channels: 9 (L1–L8 + TotalLeft) per foot
Per-subject aggregation:
→ Mean across windows
→ Std across windows
→ Skewness across windows
→ Kurtosis across windows
Final matrix: 80 subjects × ~3,000 features
Applied: z-score normalisation (StandardScaler)
Manual Features (Alternative Approach)
15 features per channel per window:
· Mean, Std, Min, Max
· Skewness, Kurtosis
· Q25, Q75 (interquartile range)
· Mean |Δ|, Std Δ (first diff)
· Range, CV (coefficient of variation)
· Signal energy (mean x²)
· Dominant frequency (FFT)
· Low-frequency energy
Advantages over TSFresh:
→ Faster (seconds vs. hours)
→ Interpretable (domain knowledge)
→ Less prone to overfitting
Final matrix: 80 subjects × 60–120 features
Applied: z-score normalisation (StandardScaler)
Three feature sets computed independently: (1) Left foot only · (2) Right foot only · (3) Combined (concatenation)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
10/18

## Slide 11
04
Dimensionality Reduction
PCA · t-SNE · Left / Right / Combined Feet · z-score normalised

## Slide 12
PCA — Left Foot Features
Features z-score normalised before PCA
04 · PCA (Left Foot)
Three panels: (A) PD/HC diagnosis · (B) Cohort — possible confound · (C) H&Y severity stage
[INSERT IMAGE] fig_E_pca_left_foot.png (Panel A: PD(red) vs HC(blue) · Panel B: Cohort colours · Panel C: H&Y scale)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
12/18

## Slide 13
PCA — Right Foot Features
Features z-score normalised before PCA
04 · PCA (Right Foot)
Three panels: (A) PD/HC diagnosis · (B) Cohort — possible confound · (C) H&Y severity stage
[INSERT IMAGE] fig_E_pca_right_foot.png (Panel A: PD(red) vs HC(blue) · Panel B: Cohort colours · Panel C: H&Y scale)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
13/18

## Slide 14
PCA — Combined Feet Features (Left + Right)
Features z-score normalised before PCA
04 · PCA (Combined)
Three panels: (A) PD/HC diagnosis · (B) Cohort — possible confound · (C) H&Y severity stage
[INSERT IMAGE] fig_E_pca_combined.png (Panel A: PD(red) vs HC(blue) · Panel B: Cohort colours · Panel C: H&Y scale)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
14/18

## Slide 15
t-SNE Embedding — Left / Right / Combined Feet
Features z-score normalised; PCA pre-compression → t-SNE
04 · t-SNE
Each plot: (A) PD/HC coloured · (B) Cohort coloured | Perplexity=20, 1000 iterations
[INSERT IMAGE] fig_F_tsne_left_foot.png (Left Foot)
Left Foot
[INSERT IMAGE] fig_F_tsne_right_foot.png (Right Foot)
Right Foot
[INSERT IMAGE] fig_F_tsne_combined.png (Combined Feet)
Combined Feet
Interpretation guide: • Good cluster separation in panel A → features distinguish PD from HC • Cluster alignment with cohort in panel B → cohort confound present (condition, not disease) • Compare left vs right vs combined to see if bilateral features help separation • Combined feet expected to show best separation (more information)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
15/18

## Slide 16
05
Alternative Approaches
UMAP · Statistical Tests · Feature Importance · Heatmaps

## Slide 17
Alternative Approaches — Beyond PCA/t-SNE
05 · Alternative Approaches
Approach 1 — UMAP (Uniform Manifold Approximation)
• Preserves both local and global structure (unlike t-SNE)
• Faster than t-SNE for large datasets
• Hyperparameters: n_neighbors=15, min_dist=0.1
• Applied to combined foot features (z-score normalised)
• Panels: (A) diagnosis (B) cohort
[INSERT IMAGE] fig_H_umap_combined.png (UMAP — Combined feet (panel A: PD/HC, panel B: cohort))
Approach 2 — Mann-Whitney U Feature Significance
• Non-parametric test: PD vs HC per feature
• No normality assumption required
• -log10(p) plotted: higher = more significant
• Red dashed line: p=0.05 | Orange: p=0.001
• Identifies which extracted features are most
discriminative between PD and HC groups
[INSERT IMAGE] fig_I_significance.png (Mann-Whitney U −log10(p) for top 15 features (combined))
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
17/18

## Slide 18
Feature Analysis — Heatmap & Distributions
05 · Feature Analysis
Feature Heatmap (Z-Score by Group)
Top 15 most discriminative features per foot condition | Higher red = PD elevated, blue = HC elevated
[INSERT IMAGE] fig_G_feature_heatmap.png (3 panels: Left foot / Right foot / Combined (rows: HC, PD))
Feature KDE Distributions
Top 6 discriminative features — KDE per group | Dashed vertical = group mean
[INSERT IMAGE] fig_H_feature_distributions.png (6 KDE plots (red=PD, blue=HC, dashed=mean))
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
18/18

## Slide 19
06
Key Findings & Next Steps
Summary of Deliverable 1 · Implications for Mamba Modelling

## Slide 20
Key Findings & Next Steps
06 · Discussion
Observations from Deliverable 1
Demographics:
• N=80 in Fold 1 (40 PD, 40 HC) — balanced
• Full dataset: 166 subjects (93 PD, 73 HC)
• H&Y severity: 19/14/7 (imbalanced → SMOTE)
Signal analysis:
• PD subjects show higher CV in force signals
• Irregular peak spacing visible in raw traces
• Consistent with Yogev 2005 variability findings
Feature extraction:
• TSFresh: ~750+ features per channel window
• Manual: 15 interpretable features per channel
• Combined feet gave richest feature set
PCA / t-SNE:
• [Fill in after running: separation observed?]
• [Cohort confound visible in panel B?]
• [Combined feet better than single foot?]
Next Steps (Deliverable 2+)
Baseline Models:
• TSFresh features + Random Forest (5-fold CV)
• TSFresh features + SVM linear & RBF (5-fold CV)
• Evaluation: Accuracy, F1, AUC, precision, recall
Mamba / SSM Models:
• Input: raw VGRF time series (multivariate)
• Window: 5s / 2.5s step (matched to TSFresh)
• Architecture: bidirectional Mamba encoder
→ binary head (PD/HC)
→ severity head (H&Y 2/2.5/3)
• Inspired by HARMamba (Li et al. 2024)
and MedMamba (He et al. 2026)
Evaluation Strategy:
• SMOTE applied on training folds only
• Cross-cohort testing (train Ga+Si, test Ju)
• Target: beat Naimi et al. 88% severity accuracy
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
20/18

## Slide 21
Vielen Dank
für Ihre Aufmerksamkeit!