## Slide 1
Deliverable 1
Data Analysis — Parkinson's Disease Gait Signal Detection
Project: State Space Models (Mamba) for Medical Time Series
Dataset: PhysioNet — Gait in Parkinson's Disease | N=166 | 5-Fold CV
May 2026 | FAU Erlangen-Nürnberg | Technische Fakultät

## Slide 2
01
Dataset Overview
Full demographics and fold split structure
02
Signal Visualization
Raw VGRF traces & variability comparison
03
Windowed TSFresh/manual features, z-score normalization
TSFresh + manual features, z-score normalisation
04
Dimensionality Reduction
PCA and t-SNE (left / right / combined)
05
Feature Diagnostics
Heatmap and combined-feature distributions
06
Key Findings
Task 1 observations and presentation takeaways
Agenda - Deliverable 1: Data Analysis

## Slide 3
01
Dataset Overview
Demographics · Cohort Structure · Label Distribution

## Slide 4
Dataset Demographics — Full Dataset (N=166)
01 · Dataset Overview
Full Dataset (from demographics.xls)
PD (n=93)
HC (n=73)
Male / Female
58 / 35
40 / 33
Age mean±SD
66.9 ± 9.7 yrs
63.3 ± 8.0 yrs
Height mean±SD
1.68 ± 0.10 m
1.68 ± 0.08 m
Weight mean±SD
72.3 ± 11.8 kg
72.3 ± 11.4 kg
H&Y mean±SD
2.26 ± 0.34
—
UPDRS-M mean±SD
18.0 ± 9.6
—
Per-Cohort Breakdown
Cohort
PD
HC
Total
Condition
Age PD
Ga (Yogev)
29
18
47
Normal walk
61.6±8.8
Si (Frenkel-Toledo)
35
29
64
Treadmill
67.2±9.1
Ju (Hausdorff)
29
26
55
RAS walk
66.8±10.8
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
4/21

## Slide 5
Dataset Demographics - 5-Fold Split Files
01 · Dataset Overview
Per-fold composition (validation included)
PD
HC
Total
Training files / fold
30
30
60
Validation files / fold
10
10
20
Test files / fold
10
10
20
Per-fold total
50
50
100
Unique subject set
50
50
100
Cohorts Ga / Si / Ju
18 / 16 / 16
13 / 21 / 16
31 / 37 / 32
PD H&Y 2.0 / 2.5 / 3.0
26 / 16 / 8
-
50 PD
Split Integrity Note
- Every fold is class-balanced: 30/30 train, 10/10 validation, 10/10 test.
- The same 100-subject balanced subset appears across the five split files.
- Validation should be used for model selection; test remains held out.
- Prepared feature figures in deliverable1_outputs are from the existing Fold 1 train+test output subset (N=80).
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
5/21

## Slide 6
02
Signal Visualization
Raw VGRF Traces · Force Variability · PD vs HC Comparison

## Slide 7
Raw VGRF Signals — PD vs Healthy Controls
15 seconds of total force, left and right foot
02 · Signal Visualization
Vertical Ground Reaction Force (VGRF) captures the force each foot exerts on the ground. 16 sensors per foot at 100 Hz. Coefficient of Variation (CV) shown per trace.
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
7/21

## Slide 8
Gait Force Variability — PD vs Healthy Control
Rolling mean ± SD (5s window, 2.5s step)
02 · Signal Visualization
Key finding (Yogev et al., 2005): In healthy adults, gait rhythmicity is automatic — stride variability is unaffected by cognitive load. In PD, variability increases markedly under dual-task conditions, indicating a loss of automaticity.
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
8/21

## Slide 9
03
Feature Extraction
TSFresh · Manual Features · Z-Score Normalisation · Per-Subject Statistics

## Slide 10
Feature Extraction Pipeline
Windowed extraction → per-subject statistics → z-score normalisation
03 · Feature Extraction
TSFresh (Primary Approach)
• Library: tsfresh (EfficientFCParameters)
• ~750+ features per channel per window
• Window: 5 seconds (500 samples)
• Step: 2.5 seconds (50% overlap)
• Channels: 9 (L1–L8 + TotalLeft) per foot
Per-subject aggregation:
→ Mean across windows
→ Std across windows
→ Skewness across windows
→ Kurtosis across windows
Final matrix: 80 subjects × ~3,000 features
Applied: z-score normalisation (StandardScaler)
Manual Features (Alternative Approach)
15 features per channel per window:
· Mean, Std, Min, Max
· Skewness, Kurtosis
· Q25, Q75 (interquartile range)
· Mean |Δ|, Std Δ (first diff)
· Range, CV (coefficient of variation)
· Signal energy (mean x²)
· Dominant frequency (FFT)
· Low-frequency energy
Advantages over TSFresh:
→ Faster (seconds vs. hours)
→ Interpretable (domain knowledge)
→ Less prone to overfitting
Final matrix: 80 subjects × 60–120 features
Applied: z-score normalisation (StandardScaler)
Three feature sets computed independently: (1) Left foot only · (2) Right foot only · (3) Combined (concatenation)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
10/21

## Slide 11
04
Dimensionality Reduction
PCA · t-SNE · Left / Right / Combined Feet · z-score normalised

## Slide 12
PCA — Left Foot Features
Features z-score normalised before PCA
04 · PCA (Left Foot)
Three panels: (A) PD/HC diagnosis · (B) Cohort — possible confound · (C) H&Y severity stage
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
12/21

## Slide 13
PCA — Right Foot Features
Features z-score normalised before PCA
04 · PCA (Right Foot)
Three panels: (A) PD/HC diagnosis · (B) Cohort — possible confound · (C) H&Y severity stage
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
13/21

## Slide 14
PCA — Combined Feet Features (Left + Right)
Features z-score normalised before PCA
04 · PCA (Combined)
Three panels: (A) PD/HC diagnosis · (B) Cohort — possible confound · (C) H&Y severity stage
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
14/21

## Slide 15
t-SNE Embedding — Left / Right / Combined Feet
Features z-score normalised; PCA pre-compression → t-SNE
04 · t-SNE
Each plot: (A) PD/HC coloured · (B) Cohort coloured | Perplexity=20, 1000 iterations
Left Foot
Right Foot
Combined Feet
Interpretation guide: • Good cluster separation in panel A → features distinguish PD from HC • Cluster alignment with cohort in panel B → cohort confound present (condition, not disease) • Compare left vs right vs combined to see if bilateral features help separation • Combined feet expected to show best separation (more information)
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
15/21

## Slide 16
05
Feature Diagnostics
Heatmaps - Feature Distributions - PCA/t-SNE Interpretation

## Slide 17
Feature Analysis - Heatmap
05 - Feature Diagnostics
Top discriminative features by foot condition
Group-wise z-score means highlight which extracted features differ between PD and healthy controls.
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
17/21

## Slide 18
Feature Distributions - Combined Feet
05 - Feature Diagnostics
KDE distributions for selected combined-foot features
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
18/21

## Slide 19
06
Key Findings
Summary of Deliverable 1 - Task 1 Presentation Takeaways

## Slide 20
Key Findings
06 · Discussion
What the data shows
Demographics:
- Full Excel cohort: 166 subjects (93 PD, 73 HC).
- Fold files use a balanced 100-subject subset.
- Each fold has 60 train, 20 validation, 20 test files.
Signal analysis:
- Raw VGRF traces show clear gait-cycle structure.
- Several PD examples show higher force variability.
- Variability plots are consistent with PD gait-rhythm disruption reported in the literature.
Feature space:
- Features are z-score normalized before PCA/t-SNE.
- Left, right, and combined-foot views are analyzed separately.
Presentation takeaway
Main message for Task 1:
- The dataset is usable and the official split structure is balanced.
- PCA/t-SNE show partial visual structure, not perfect PD/HC separation.
- Cohort effects remain visible and should be controlled in later modeling.
Recommended next analysis checks:
- Regenerate final feature figures with validation included if the presentation must reflect all fold files.
- Keep train/validation/test boundaries fixed for future model evaluation.
- Report model results by fold and inspect cohort-specific behavior.
Deliverable 1 — PD Gait Analysis | FAU Erlangen-Nürnberg
20/21

## Slide 21
Thank you
for your attention!